## Slide 1: Comcast Trove Design Proposal (draft)

## Slide 2: 0.96 PB Ceph + 2.1 PB Swift backup* (2 Racks)
OpenStack Compute
Trove VM
OpenStack Controller
(OpenStack services & Ceph monitor)
OpenStack Controller
(OpenStack services & Ceph monitor)
OpenStack Controller
(OpenStack Svcs & Ceph monitor + Op Mgmt)
Swift Proxy
Swift Object
Swift Object
Ceph block
(OSD)
Ceph block
(OSD)
Ceph block
(OSD)
OpenStack Compute
Trove VM
OpenStack Compute
Trove VM
OpenStack Compute
Trove VM
10 Gb
10 Gb
Mellanox SX1410, Qty 2
1 Gb
Mellanox 8891-S52, Qty 2
One Per Rack
Ceph block
(OSD)
Swift Object
Swift Metadata
High Level Network Architecture Diagram
Per Server Node
2x10G DAC Cables
2x 1G Cat5e Cables
2x10G
2x1G
** Possible Configure 2x40G per node for Controller, Proxy & Object
**
**
**
OS provisioning
IPMI
Data
2x 56G ISL
Customer Up-Links

## Slide 3: Racking / Config
Rack:
QTY: 2
SlimRack 7965-94Y
PDUs
Network Option 1: (HA)
2 x Mellanox SX1410 (8831-S48)
1*x Mellanox (8891-S52) (* per rack)
Network Option 2: (non HA)
1 x Mellanox SX1410 (8831-S48)
2* x Mellanox (8891-S52) (* per rack)
Swift Object /MetaData
QTY: 3
Per Server Config: (Briggs 8001-21C) (2U)
20 Cores ( 2.0Ghz), 256GB ,
(OS) 2+ 128GB DOM + (Meta) 2/4 x NvMe 800GB (cache) (3 & 5 DWPD or SSDs
2 x 2-Port 10G NIC ( Intel/Mellanox)
Expansion Drawer (4U)
90 LFF – 8TB SATA HDDs
CEPH Config :
QTY: 12
Per Server Config: (Briggs 8001-22C) (2U)
20 Cores ( 2.92Ghz), 256GB ,
(OS) 2+ 128GB DOM + (Meta) 2x SSD 800GB (cache) (1.2 DWPD) + (Storage)10 x 8TB HDDs (~80TB)
2 x 2-Port 10G NIC ( Intel/Mellanox)
OpenStack Compute:
QTY: 12
Server Config: (Stratton 8001-12C) (1U)
16 Cores ( 2.3Ghz), 128GB ,
2 x 4TB Sata HDDs
2 x 2-Port 10G NIC ( Intel 10G/Mellanox)
OpenStack Controller:
QTY: 3
Server Config: (Stratton 8001-12C)
16 Cores ( 2.3Ghz), 128GB ,
2 x 4TB Sata HDDs
2 x 2-Port 10G NIC ( Intel 10G/Mellanox)
Swift Proxy:
QTY: 3
Server Config: (Stratton 8001-12C) (1U)
20 Cores ( 2.922Ghz), 256GB ,
2 x 4TB Sata HDDs
2 x 2-Port 10G NIC ( Intel 10G/Mellanox)
**Notes:
Openstack & Proxy Node can be combined (if requires lesser than 24 SWIFT Objects)
Compute qty + Memory config change is required base on actual Database Performance requirement
Dedicated Swift Meta Data Server maybe required
See Notes: **