## Slide 1: Accelerated DB Design proposal

## Slide 2
Deployer (Power8-LC or x86)
Ceph block
(OSD)
Ceph block
(OSD)
10 Gb
Lenovo G8264CS
1 Gb
Lenovo G8052
8335-GTB
High Level Network Architecture Diagram
Per Server Node
2x10G DAC Cables
2x 1G Cat5e Cables
2x10G
2x1G
OS provisioning
IPMI
Data
Customer Up-Links

## Slide 3: Racking / Configuration
Rack:
QTY: 1
SlimRack 7965-94Y
PDUs
Network:
1 x Lenovo G8264CS (10G data network)
1*x Lenovo G8052 (1G management network)
Compute Node:
QTY: 4
Server Config:
Minsky 8335GTB (2U)
Processor – POWER8 10 Cores ( 3.492Ghz)
GPU – 4 x Nvidia GP100
Memory - 1 TB ,
2 x 3.8TB Sata HDDs
1 x PCIe2 10GbE SFP+ CU 4-port converged network adapter
Deployment Node (Power8 – LC Option ):
QTY: 1
Habanero S812LC(8348-21C) tested
Should support any Power8-LC system
Deployment Node (x86 option):
QTY: 1
Server Config:
Lenovo M4
Processor - 2 Cores
Memory – 32GB
1 x 1 TB Sata HDDs
2 x 2-Port 10G NIC ( Intel 10G/Mellanox)